## Slide 1: Why do we have EIRP Limits?
William Stucke
FWTF V
12th May 2016
Century City, Cape Town

## Slide 2: What is EIRP?
Effective (or Equivalent) Isotropic Radiated Power
Conceptually, consider an antenna as a point source

## Slide 3: Calculating EIRP
Simple equation:
EIRP = Transmitted Power – Cable Losses + Antenna Gain
Measured in dBm or dBW
1 dBW = 30 dBm
Antenna gain measured in dBi

## Slide 4: Dipole Antenna
At Length = 0.48 λ, Zin = 70 Ω
Zin = 73 + j42.5 Ω

## Slide 5: Antenna Gain
Antenna gain is calculated as compared to a theoretical spherical radiation pattern
A simple dipole antenna flattens the sphere into a doughnut and may give a gain of up to about 8 dBi

## Slide 6: Dipole antenna

## Slide 7: Dipole antenna

## Slide 8: Yagi-Uda Antenna
Invented in 1928, but only translated into English much later
Gives a gain of up to 20 dBi
Can receive weaker signals
Simple construction – made of metal rods
Highly directional
Reduces sensitivity to interference

## Slide 9: Yagi-Uda Antenna

## Slide 10: Yagi-Uda Antenna
Reflectors - longer than driven element = Inductive
Directors - shorter than driven element = Capacitive

## Slide 11: Yagi-Uda Antenna

## Slide 12
Idealised Coverage
Omni Antenna Sector Antenna

## Slide 13: Real Coverage Example

## Slide 14: Real Coverage Example 2

## Slide 15: Why Specify EIRP Limits?
A simple and robust method of limiting transmitted power
Important in terms of reducing interference, especially for PtMP, as it reduces the effective range
Easy to set, easy to define, easy to measure
Not always appropriate for PtP uses

## Slide 16: Licence-Exempt Bands
Band | Type | Limit | Comment
2400 – 2483.5 MHz | WLAN | 100 mW | 20 dBm EIRP
5470 – 5725 MHz | WAS & RLAN | 1 W | 30 dBm EIRP PtMP
5725 – 5850 MHz | WAS & RLAN | 4 W EIRP 1 W Tx power | Tx output spectral density < 8 dBm in any 3 kHz band.
5725 – 5850 MHz | BFWA | 200 W EIRP 1 W Tx power | Tx output spectral density < 8 dBm in any 3 kHz band.
17.1 – 17.3 GHz | HiperLAN | 100 mW EIRP | 

## Slide 17: Licence-Exempt Bands
Band | Type | Limit | Comment
24.00 – 24.25 GHz | SRD |  | Not approved by ICASA for PtP or PtMP
57.00 – 64 GHz | PtP | 55 dBm EIRP | ICASA revising – V Band
57.00 – 66 GHz | MGWS | 40 dBm | ICASA revising
71-76 GHz and 81-86 GHz |  |  | E Band - PtP

## Slide 18: A little History
FCC use “Part 15” to regulate these bands
Recently reduced EIRP limits in the 5 GHz band
ICASA revising V & E bands

## Slide 19: High Gain Antenna PtP Link
Red Antenna points beam at Blue antenna. Blue antenna points back. High gain means that: -
  Better reception at a distance, without higher transmitted power
  Good rejection of incident signals from other directions
Notes: Curve represents a Dish antenna
Triangle represents the beam transmitted by the dish antenna
The two dishes are aimed accurately at each other. Red antenna may have as much as 30dB gain for the Blue antenna, compared to signals from other directions. Similarly for the Blue antenna selectively receiving the Red signal.

## Slide 20: Many PtP Links
Notes: Many PtP Links can exist in the same geographical area, even with exactly the same frequency. Provided these links either don’t cross at all, or cross at a sufficiently oblique angle, there is no problem. However, if two beams are very close to each other in both position and angle, there is a danger of interference between the two beams. This is highlighted by the grey oval.
The process of calculating if any interference is likely to occur between uses of a frequency is called “coordination”. It is computationally intensive, and takes some time to complete. With today’s equipment, you can expect to coordinate perhaps 200 uses in 24 hours of server time.

## Slide 21: What do we need to change?
EIRP limitations on PtP links – to allow more directional antennas
  Longer range
  Better directionality
  Better interference resistance
  Less interference caused
Introduce dynamic spectrum assignment – White Spaces